## Slide 1
Special and Diving Operation
Submarine Rescue Ship
SDO-SuRS
Secretariat General of Defence / National Armaments Directorate
Cdr Emanuele DE MINICIS
Head of International Cooperations Service
Notes: 1

## Slide 2
AGENDA
Mission
Special operations
Diving Operations
Submarine Rescue assets
Conclusion

## Slide 3
MISSION

## Slide 4
MISSION
Support Unit for the Diving Operations Group (GOS) of the Italian Navy for Diving Operation (DO);
Support Unit for operational/training activities, with an underwater/amphibious connotation, of Special Forces (GOI) for Special Operation (SO);
Capability to carry on operative and training activities for distressed submarines (Submarine Rescue Ship - SuRS) up to the NATO standards deep (600 m);
Complex Command for Special Forces operations up to JSOCC (Joint Special Operation Component Command) level.

## Slide 5
PROGRAMME LAYDOWN
Delivery
End of Temporary Support
2026
2033
2024
Launch
Apr 2023
Keel Laying
Dec 2021
Contract signed

## Slide 6
Dimensions
Δ 12000 t
L 128,5 m
B 24 m
Working deck 40 x 24 m
Propulsions
Full Electric (6 x 2,5MW DDGG +
2 x 5MW pods + 3 x 1,5 MW thrusters)
Vmax 17 kts
Range 5000 nm @ 16 kts
DPS: IMO DP3
Accomodations
Crew 120
Accomodations 200
Capability
Submarine Rescue up to 600 m
MED NATO Role 2B
Diving ops up to 300 m
Spec Ops support + JSOCC
Rescue ship
Submarine Rescue Vehicle con LARS
VoO for NSRS e SDRS
Submarine Rescue Chamber
Insufflation system for DISSUB
Decompression chambers for 60 persons
Diving
2 ADS suite + LARS
AHC off shore 100 t @ 15 m
AHC off shore 40 t @ 15 m
Working+watching ROVs
Integrated diving system with moonpool
SHIP OVERVIEW

## Slide 7
POD SYSTEM
TUNNEL THRUSTER
2 x 5,5 MW
KONGSBERG PULLING POD 1380-O/M
3 x 1,5 MW
KONGSBERG TT2650 DPN FP
PROPULSION
6 x 2,6 MW
WARTSILA 8L26
COMF-NOISE-A
COMF-VIB-A
GREENPLUS
DP3

## Slide 8
electroacoustic sensors

## Slide 9
mariottiyard.it
UTC ROOM

## Slide 10
SPECIAL OPERATIONS (SO)
The Unit will have the capability to operate as a Special Forces Command Unit up to Task Group level and to transport and deploy vehicles and special assets on Working Deck e.g.:
RHIB model Hurricane or similar
ISO Container assets

## Slide 11
DIVING OPERATIONS (DO)
The Unit may be deployed in shallow and deep-waters search operations, in the context of Homeland Security i.e.:
oil pipeline and oil/gas terminals surveillance operations;
anti-terrorism/sabotage function;
search operations for dangerous wrecks, recovery from the seabed and retrieval of sites at high environmental risk..

## Slide 12
SAT DIVING SYSTEM
Hyperbaric Chambers 2 X 6
DIVING BELL (SDC) & LARS da Moonpool
Hyperbaric Life Boat (12 + 4 people)
Dive Control Panel
SDC Analysis Panel
Gas Storage 32 x 2.8 m3 200 bar cylinders
DIVING OPERATIONS (DO)

## Slide 13
Diving Control room
DIVING OPERATIONS (DO)

## Slide 14
SUBMARINE RESCUE SHIP (SuRS)
Submarine Assistance Ventilation
Equipment Rescue (SAVER)
Notes: 14

## Slide 15
Portable Launch and Recovery System (PLARS)
Deck Decompression Chambers (DDC)
Submarine Rescue Vehicle (SRV)
DEPLOYABLE SUBMARINE RESCUE ASSETS

## Slide 16
SUBMARINE VENTILATION SYSTEM (SVS)
SUBMARINE RESCUE CHAMBER (SRC)
WROV with LARS
WROV
DEPLOYABLE SUBMARINE RESCUE ASSETS

## Slide 17: FASD - FAST AUXILIARY SYSTEMS DEPLOY
3
9
2
1
4
5
6
7
8
10
1
1
ISO Standard Containers (10, 20, 40 feet)
Auxiliary System (Breathable air and mix gas)
Diesel electric power station
Electric distribution system
Operation monitoring Central Unit
Total ISO container 10 + 1 Air module
MODULAR concept

## Slide 18: CONCLUSION
State-of-the-art in UW capabilities
High value of interoperability and deployability
Full spectrum Hub in UW domain
Fostering Multinational cooperation

## Slide 19
THANK YOU FOR YOUR KIND ATTENTION
Secretariat General of Defence / National Armaments Directorate
Cdr Emanuele DE MINICIS
Head of International Cooperations Service
email: r1coordcs@navarm.difesa.it

## Slide 20
Secretariat General of Defence / National Armaments Directorate
Special and Diving Operation
Submarine Rescue Ship
SDO-SuRS
Cdr Emanuele DE MINICIS
Head of International Cooperations Service
Notes: 20