## Slide 1
REDUCING OUR CARBON FOOTPRINT WITH TILE AND STONE
Provider

## Slide 2: INHERENT SUSTAINABLE ATTRIBUTES OF TILE

## Slide 3
TILE | INHERENT SUSTAINABLE ATTRIBUTES
Manufactured with materials that are natural and plentiful
Clay
Kaolin
Feldspar
Production waste
Materials reused from other industries

## Slide 4
TILE | INHERENT SUSTAINABLE ATTRIBUTES
Manufactured with materials that are recycled and reused
Production waste
Materials reused from other industries

## Slide 5
TILE | INHERENT SUSTAINABLE ATTRIBUTES
Manufactured locally

## Slide 6
TILE | INHERENT SUSTAINABLE ATTRIBUTES
Moisture tolerant

## Slide 7
TILE | INHERENT SUSTAINABLE ATTRIBUTES
Impact and abrasion resistant

## Slide 8
TILE | INHERENT SUSTAINABLE ATTRIBUTES
Non-combustible

## Slide 9
TILE | INHERENT SUSTAINABLE ATTRIBUTES
Mold resistant

## Slide 10
TILE | INHERENT SUSTAINABLE ATTRIBUTES
Non emitting; contributes to indoor air quality

## Slide 11
TILE | INHERENT SUSTAINABLE ATTRIBUTES
Easy to clean and maintain
Notes: Source: TCNA, Chitty, Griese: Selling Tile Post Pandemic, Coverings Connected 2020

## Slide 12
TILE | INHERENT SUSTAINABLE ATTRIBUTES
Inhospitable to bacteria

## Slide 13
TILE | INHERENT SUSTAINABLE ATTRIBUTES
Durable

## Slide 14
TILE | INHERENT SUSTAINABLE ATTRIBUTES
Competitive life cycle cost

## Slide 15: MANUFACTURING AND MATERIAL INGREDIENTS

## Slide 16
MANUFACTURE OF TILE
Raw materials
From the industry-wide EPD for ceramic tiles manufactured in North America
Notes: This table is from the industry-wide EPD for ceramic tiles manufactured in North America. The general composition is presented as a production-weighted average to protect the confidentiality of the composition of individual manufacturers’ products.
Clay - Wikipedia
Wikipediahttps://en.wikipedia.org › wiki › Clay
Clay is a type of fine-grained natural soil material containing clay minerals (hydrous aluminium phyllosilicates, e.g. kaolinite, Al2Si2O5(OH)4).

## Slide 17
MANUFACTURE OF TILE
Clay
Kaolin
Feldspar
Raw materials
Notes: Conceptual slides on the manufacture of tile are from Ceramics of Italy YouTube video, https://www.youtube.com/watch?v=87ca2H2LtzY&t=332s
Clay - Wikipedia
Wikipediahttps://en.wikipedia.org › wiki › Clay
Clay is a type of fine-grained natural soil material containing clay minerals (hydrous aluminium phyllosilicates, e.g. kaolinite, Al2Si2O5(OH)4).

## Slide 18
Clay
Kaolin
Feldspar
Production waste
Materials reused from other industries
MANUFACTURE OF TILE
Raw materials
Notes: By reusing construction waste and materials from other industries. This way we reduce the consumption of raw materials and the CO2 emissions deriving from transport.
Conceptual slides on the manufacture of tile are from Ceramics of Italy YouTube video, https://www.youtube.com/watch?v=87ca2H2LtzY&t=332s

## Slide 19
MANUFACTURE OF TILE
BATCHING
Raw materials are mixed, ground, and pulverized
100% of the wastewater discharged from the production process is retrieved
Mixing, grinding, creating slurry
Water is added to form a slurry
Notes: Conceptual slides on the manufacture of tile are from Ceramics of Italy YouTube video, https://www.youtube.com/watch?v=87ca2H2LtzY&t=332s

## Slide 20
MANUFACTURE OF TILE
Slurry is spray-dried with a quick-drying process
Drying
Notes: Conceptual slides on the manufacture of tile are from Ceramics of Italy YouTube video, https://www.youtube.com/watch?v=87ca2H2LtzY&t=332s

## Slide 21
MANUFACTURE OF TILE
Water is eliminated leaving a fine powder
Slurry is spray-dried with a quick-drying process
Drying
Notes: Conceptual slides on the manufacture of tile are from Ceramics of Italy YouTube video, https://www.youtube.com/watch?v=87ca2H2LtzY&t=332s

## Slide 22
MANUFACTURE OF TILE
Spray-dried powder is placed into a die
Pressing
Notes: Conceptual slides on the manufacture of tile are from Ceramics of Italy YouTube video, https://www.youtube.com/watch?v=87ca2H2LtzY&t=332s

## Slide 23
MANUFACTURE OF TILE
Spray-dried powder is placed into a die
Spray-dried powder is pressed…
Pressing
Notes: Conceptual slides on the manufacture of tile are from Ceramics of Italy YouTube video, https://www.youtube.com/watch?v=87ca2H2LtzY&t=332s

## Slide 24
MANUFACTURE OF TILE
Spray-dried powder is placed into a die
Spray-dried powder is pressed…
to create the formed product
Pressing
Notes: Conceptual slides on the manufacture of tile are from Ceramics of Italy YouTube video, https://www.youtube.com/watch?v=87ca2H2LtzY&t=332s

## Slide 25
MANUFACTURE OF TILE
Tile is dried
Drying
Notes: Conceptual slides on the manufacture of tile are from Ceramics of Italy YouTube video, https://www.youtube.com/watch?v=87ca2H2LtzY&t=332s

## Slide 26
MANUFACTURE OF TILE
Tile is glazed
Glazing
Notes: Conceptual slides on the manufacture of tile are from Ceramics of Italy YouTube video, https://www.youtube.com/watch?v=87ca2H2LtzY&t=332s

## Slide 27
MANUFACTURE OF TILE
Tile is fired; this is the most process that requires the most amount of energy.
Roller kiln technology has reduced firing times.
Heat recovery technologies have reduced energy consumption 47% since 1980.
Firing
Notes: Conceptual slides on the manufacture of tile are from Ceramics of Italy YouTube video, https://www.youtube.com/watch?v=87ca2H2LtzY&t=332s

## Slide 28
MANUFACTURE OF TILE
During firing, 99% of dust emissions are captured using abatement filters.
Firing
Notes: Conceptual slides on the manufacture of tile are from Ceramics of Italy YouTube video, https://www.youtube.com/watch?v=87ca2H2LtzY&t=332s

## Slide 29
What is transparency?
MATERIAL INGREDIENT TRANSPARENCY
https://www.aia.org/pages/150126-how-materials-transparency-affects-your-pra
Notes: Why should I care about a resource for manufacturers if I’m not a manufacturer?

## Slide 30
Why is transparency important?
MATERIAL INGREDIENT TRANSPARANCY
Material ingredient transparency is a fundamental step manufacturers take toward compliance with green and healthy building certification programs.
LEED
WELL
Living Building Challenge (LBC)
… others
Notes: Why should I care about a resource for manufacturers if I’m not a manufacturer?

## Slide 31
MATERIAL INGREDIENT GUIDE
What is the Material Ingredient Guide?
Why should I care about a resource for manufacturers?
A resource for ceramic tile, mortar, and grout manufacturers to use when providing the content and chemical makeup of their products.
Health Product Declaration (HPD)
Manufacturer Inventory (MI)
Uses standard reporting formats:
Notes: Why should I care about a resource for manufacturers if I’m not a manufacturer?

## Slide 32
Who is behind it?
MATERIAL INGREDIENT GUIDE
17 manufacturers collaborated on crowdfunding GreenScreen® benchmark scores.
Participants & Supporters
Initiative of the Tile Council of North America (TCNA).
Notes: Greenscreen benchmark scores

## Slide 33
MATERIAL INGREDIENT GUIDE | FOUR STEPS OF TRANSPARENCY
These steps guide ceramic tile, mortar, and grout manufacturers in developing material ingredient reports using formats such as HPD and MI that satisfy common A&D criteria.

## Slide 34
MATERIAL INGREDIENT GUIDE | STEP 1: INVENTORY
For all building products, the risk of chemical exposure should be considered high unless proven otherwise.
Chemicals are required to be inventoried if present at minimum threshold.
Manufacturers must identify the substances used in their products to a threshold of 1,000 ppm or 100 ppm.
Notes: It is important to note that 100ppm is more stringent and requires
inventorying substances present at lower concentrations than a threshold of 1,000 ppm, and
hence, is likely to require inventorying more substances. WAP Sustainability recommends that
manufacturers target a threshold of 100 ppm for all intentionally added substances to maximize
contribution toward green and healthy building program requirements. Additionally,
concentrations can be expressed as percentages, with 100 ppm = 0.01%, 1,000 ppm = 0.1%,
and 10,000 ppm = 1.0%.

## Slide 35
MATERIAL INGREDIENT GUIDE | STEP 1: INVENTORY
1,000 ppm level requires knowledge of intentionally added ingredients to 99.9%
Inventory Thresholds
100 ppm level requires knowledge of intentionally added ingredients to 99.99%
Notes: It is important to note that 100ppm is more stringent and requires
inventorying substances present at lower concentrations than a threshold of 1,000 ppm, and
hence, is likely to require inventorying more substances. WAP Sustainability recommends that
manufacturers target a threshold of 100 ppm for all intentionally added substances to maximize
contribution toward green and healthy building program requirements. Additionally,
concentrations can be expressed as percentages, with 100 ppm = 0.01%, 1,000 ppm = 0.1%,
and 10,000 ppm = 1.0%.

## Slide 36
Tile
Mortar
Feldspar
Portland cement
Quartz, aluminum oxide, calcium oxide, potassium oxide, sodium oxide
Calcium oxide, quartz, aluminum oxide, iron oxide, sulfur trioxide
MATERIAL INGREDIENT GUIDE | STEP 1: INVENTORY
Notes: Feldspar is a group of naturally occurring aluminosilicate minerals, meaning they contain aluminum, silicon, and oxygen, as well as various amounts of potassium, sodium, and calcium. Specifically, the three compositional endmembers of feldspar are K-feldspar (KAlSi3O8), albite (NaAlSi3O8), and anorthite (CaAl2Si2O8)

## Slide 37
MATERIAL INGREDIENT GUIDE | STEP 1: INVENTORY
Table 2-1: Mixture compositions
Table 2-2: List of chemicals common to ceramic tile, mortar, and/or grout
Notes: CASRN = Chemical Abstracts Service Registry Number

## Slide 38
MATERIAL INGREDIENT GUIDE | STEP 1: INVENTORY
Example of manufacturer inventory report
Notes: Received from Jim Whitfield, Mapei, 3/8/23
CASRN = Chemical Abstracts Service Registry Number

## Slide 39
MATERIAL INGREDIENT GUIDE | STEP 2: SCREEN & ASSESS
Evaluate the toxicological profile associated with the individual CASRN identified for each substance in the inventory
Various screening methods from basic automated online tools to GreenScreen® assessment
Notes: CASRN = Chemical Abstracts Service Registry Number

## Slide 40
Each chemical evaluated under GreenScreen® is assigned a Benchmark between 1 and 4.
The Benchmark score is determined by analyzing specific combinations of hazard classifications for the 18 endpoints included in GreenScreen.
A higher benchmark indicates progressively safer chemicals.
MATERIAL INGREDIENT | GREENSCREEN BENCHMARK SCORES
https://www.greenscreenchemicals.org/learn/full-greenscreen-method
Notes: https://www.greenscreenchemicals.org/learn/full-greenscreen-method
PERSISTENCE: “The length of time the chemical can exist in the environment before being
destroyed (i.e., transformed) by natural processes.” (USEPA, https://www.epa.
gov/sites/production/files/2014-01/documents/aa_criteria_v2.pdf, accessed
9/20/17)
BIOACCUMULATION: “A process in which a chemical substance is absorbed in an organism by all routes
of exposure as occurs in the natural environment (e.g., dietary and ambient environment
sources). Bioaccumulation is the net result of competing processes of
chemical uptake into the organism at the respiratory surface and from the diet
and chemical elimination from the organism including respiratory exchange, fecal
egestion, metabolic biotransformation of the parent compound and growth dilution.”
(Arnot, J.A. and F.A. Gobas, A review of bioconcentration factor (BCF) and bioaccumulation
factor (BAF) assessments for organic chemicals in aquatic organisms.

## Slide 41
MATERIAL INGREDIENT GUIDE | STEP 3: DISCLOSE
If transparency is a trust virtue, then disclosure is the tool to achieve that trust.
Ingredient information is disclosable using reporting formats widely accepted as transparent by green and healthy building certification programs:
Consistency in disclosure is a necessary condition for transparency.
Health Product Declarations (HPDs)
Manufacturer Inventories (MIs)
Notes: Disclosure also creates an opportunity for the tile industry for three reasons: 1) the majority of
ingredients used by ceramic tile, mortar, and grout manufacturers have been inventoried,
screened, and fully assessed; 2) substance-level breakdown of the ingredients common to
ceramic tile, mortar, and grout is achievable and well-understood; 3) industry ingredient
information is disclosable using reporting formats widely accepted as transparent by green and
healthy building certification programs.

## Slide 42
MATERIAL INGREDIENT GUIDE | HEALTH PRODUCT DECLARATION (HPD)
A voluntary technical specification for reporting information on product content associated with health information.
What is an HPD?
The most recognized and widely adopted material ingredient reporting format for disclosure throughout the building and construction supply chain.
Can be used to accrue credits in LEED and other rating systems.
A third party verification program (3PV) independently reviews and verifies completed HPDs.
Notes: WAP Consulting provides 3PV for TCNA Material Ingredient Guide participants

## Slide 43
A voluntary, 3rd party-verified material ingredient report that serves as a tool for providing transparency about the ingredients in building products.
An HPD for natural stone includes details such as the mineral composition, quarry location, and any additional treatments or finishes applied to the stone.
NSI member quarriers can create HPDs for their products using NSI’s HPD Builder tool. All members’ HPDs are available on NSI’s Sustainability Resources web page.
What is an HPD?
TRANSPARENCY | HEALTH PRODUCT DECLARATION (HPD)
Notes: From the NSI website:
Health Product Declarations
A Health Product Declaration (HPD) is a material ingredient report that serves as a tool for providing transparency about the ingredients in building products. An HPD for natural stone includes details such as the mineral composition, quarry location, and any additional treatments or finishes applied to the stone.
Natural Stone Institute member quarriers can use the steps below to easily create HPDs for their products. Once published, they will be publicly available in the HPD Public Repository providing visibility to design teams. With access to the HPDs they are able to check boxes needed to satisfy green building goals including LEED credits.
How to create a material ingredient report for your natural stone product(s):
Step 1: Review NSI’s HPD Templates.
Step 2: Register to use the HPD Builder.
Step 3: Purchase tokens ($375 for 5 HPDs) or become a member of HPDC (starting at $750 for unlimited HPDs).
Step 4: Email HPDC to request NSI’s HPD Templates be added to your HPD Builder account. Be sure to let them know which one(s) you need (limestone, granite, marble, etc).
Step 5: Customize the following fields in the HPDC dashboard:
(see sample forms, next slides)
Step 6: Click through the rest of the fields in the builder and edit as needed. Refer to the HPD Open Standard, if needed, and utilize their Knowledge Base for troubleshooting.
Step 7: Publish your HPDs. This will make them publicly available in the HPD Repository. You can also download them for use on your website and sharing with clients. Send them to the Natural Stone Institute for inclusion on our Sustainability Resources webpage.

## Slide 44
HPD example
Notes: WAP Consulting provides 3PV for TCNA Material Ingredient Guide participants

## Slide 45
HPD example (supplier):
Lyons Sandstone
TRANSPARENCY | SUPPLIER HPD
Notes: This is a sample HPD from Polycor for their limestone material. Does “SC” indicate “special condition”

## Slide 46
Declare label example: Limestone (Coldspring)
TRANSPARENCY | DECLARE LABEL
Notes: I need help interpreting this.

## Slide 47
MATERIAL INGREDIENT GUIDE | STEP 4: OPTIMIZE
Optimization involves selecting products with the most thorough material ingredient reports.
Green and healthy rating programs incentivize optimization. We’ll look at LEED v4 as an example.

## Slide 48
Regarding the use of building products that exhibit material ingredient transparency, a project can earn up to two points:
MATERIAL INGREDIENT GUIDE | STEP 4: OPTIMIZE
20 different permanently installed products from at least 5 manufacturers use a LEED-specified material ingredient reporting format (HPD or MI) to disclose product ingredients to at least 1,000 ppm
5 different permanently installed products from at least 3 manufacturers satisfy other optimization pathways. This can be achieved by disclosing product ingredients at the substance level of 100 ppm
Material Ingredient Reporting
1 point
Material Ingredient Optimization
1 additional point

## Slide 49
Does the product disclose material ingredients to at least 0.1% (1000 ppm) via HPD, MI, Declare Label, etc.?
TRANSPARENCY | STEP 4: OPTIMIZE
MATERIALS REPORTING FORM
Notes: Who are making those requests?

## Slide 50
RATINGS SYSTEMS | LBC & IWBI
Living Building Challenge
International Well Building Institute
WELL Material Ingredient Transparency criteria are harmonized with LEED’s criteria with multiple levels of credit for manufacturers who effectuate higher levels of product ingredient reporting or third party verification.
The International Living Future Institute (ILFI) and the LBC are the primary stewards of “The Red List,” a list of harmful chemicals and ingredients commonly used. LBC requires all products to be Red List Free or LBC Compliant using its own reporting format, the Declare Label.
Notes: International Living Future Institute (ILFI) Living Building Challenge (LBC)

## Slide 51
Unlike competing products, many of which contain plasticizers and other synthetic materials, ceramic tile is completely inert and contains no VOCs.
Ceramic tile is composed of naturally occurring materials extracted from the surface of the earth.
Inherently non-emitting
No hazardous ingredients
TCNA
MATERIAL INGREDIENTS | FLOORING COMPARISON
Notes: From LinkedIn

## Slide 52: ENVIRONMENTAL PRODUCT DECLARATIONS (EPDs)

## Slide 53
EPDs | ENVIRONMENTAL PRODUCT DECLARATIONS
There is a growing need among specifiers and designers for quantitative reporting of the impacts of products so the environmental footprint of a building can be calculated.

## Slide 54
An EPD is a summary of the many ways the production, distribution, use, and disposal of a particular product can impact people and the planet.
What is an EPD?
https://www.greenbuildingadvisor.com/article/a-guide-to-environmental-product-declarations
EPDs | ENVIRONMENTAL PRODUCT DECLARATIONS
Notes: https://www.greenbuildingadvisor.com/article/a-guide-to-environmental-product-declarations
An EPD should answer questions like: Is the product high in embodied carbon? Is itmade with renewable materials? Will it degrade atmospheric ozone? Making it ieasier for consumers and specifiers to make the most appropriate choices.

## Slide 55
An EPD is a vehicle for reporting product environmental data in a standardized manner.
EPDs provide a common framework for reporting across major environmental impact categories.
Life Cycle Assessment (LCAs) are the building blocks of EPDs.
What is an EPD?
EPDs | ENVIRONMENTAL PRODUCT DECLARATIONS

## Slide 56
A standardized, science-based method for quantifying all the lifetime environmental impacts a product contributes throughout its life.
When applied to a building it is a building LCA.
LIFE CYCLE ASSESSMENT (LCA)
What is an LCA?
Notes: https://www.oneclicklca.com/life-cycle-assessment-explained/?utm_source=Google&utm_medium=cpc&utm_campaign=sitelink&gclid=CjwKCAjw79iaBhAJEiwAPYwoCLuedK31V1KHVSXmweTb5CYO-Kv-nW34Gi6fE5xHRX49XG_GpAtocBoC3ekQAvD_BwE
What it is: A Life Cycle Assessment (LCA) measures the environmental impacts of a product or service.
Measures both a building’s lifetime impacts and quantifies impact of individual building materials.
Takes into consideration all the steps that lead from raw material through manufacture, distribution, usage, to final disposal.
Why are we talking about it? - Well its tied to carbon and energy and wellness. Its how we are going to measure this stuff. Embodied carbon is inherently connected to climate justice and issues of public health and equity.
Benefits:
LCA allows decision makers to compare two products and to select the product that has the lowest impact on the environment.
An LCA may also provide insight in how to improve processes to achieve reduced environmental effects.
Calculate environmental impact to help find most sustainable options.

## Slide 57
Emissions are categorized in 4 stages
LIFE CYCLE ASSESSMENT (LCA) | EMISSION STAGES
Product Stage (A1-3)
Construction Stage (A4-5)
Use Stage (B1-5)
End of life Stage (C1-4)
Reuse/Recycling (D)
https://academy.oneclicklca.com/courses/take/onboarding-building-lca/texts/36851343-life-cycle-assessment-carbon-studies
GWP unit: (kgCO2e)
Kilograms of carbon dioxide equivalents
Notes: To calculate the final results of your LCA, you’ll add up the emissions from all of the life-cycle stages to get the total impacts for your project. This is typically referenced in kilograms of carbon dioxide equivalents (kgCO2e) if we’re focusing on Global Warming Potential (GWP), but we can also get results for other impact categories such as acidification or ozone depletion.
Life Cycle Stage D is benefits beyond the boundary like reuse-recycling potential.

## Slide 58
LIFE CYCLE ASSESSMENT (LCA)
Notes: THE ORIGIN OF THIS TABLE IS FIG 2: ISO 21930

## Slide 59
Two types of EPDs
Single-company, single-product EPD, the most common type. It describes the life cycle environmental impact of one product from a single manufacturer, or very similar products from a single manufacturer
Industry-wide EPD covers a general product category. These are developed by an industry association or trade group and describe an “average” product made by a number of companies in a clearly defined category
EPDs | ENVIRONMENTAL PRODUCT DECLARATIONS
Notes: https://www.greenbuildingadvisor.com/article/a-guide-to-environmental-product-declarations

## Slide 60
Provide comprehensive overview of how these products, on average per installed square meter, impact the environment over an estimated building service life of 75 years
Industry-wide EPDs
TCNA and its members have developed industry-wide EPDs for ceramic tile, mortar, and grout
Manufacturers provided data on their materials and operations and participated in a cradle-to-grave evaluation of their products, from raw material extraction through manufacturing , delivery, installation, use, and end of life
EPDs | ENVIRONMENTAL PRODUCT DECLARATIONS
Notes: https://www.greenbuildingadvisor.com/article/a-guide-to-environmental-product-declarations

## Slide 61
Product category rules (PCR) set the basis for measuring the environmental attributes of products in a certain group.
How is an EPD developed?
Manufacturer (with or without the help of consultants and/or software) develops LCA to serve as the framework for the EPD.
This information is verified by an independent third party (e.g. ASTM, UL, or NSF) to make sure they conform to ISO 14025.
https://www.greenbuildingadvisor.com/article/a-guide-to-environmental-product-declarations
EPDs | ENVIRONMENTAL PRODUCT DECLARATIONS
Notes: https://www.greenbuildingadvisor.com/article/a-guide-to-environmental-product-declarations

## Slide 62
INDUSTRY-WIDE EPD | TILE (2020)
American Wonder Porcelain
Arto Brick
Crossville
Dal-Tile Corporation
Del Conca USA
Florida Tile
Interceramica
Ironrock
Porcelanite-Lamosa
Portobello America
Quarry Tile Co.
StonePeak Ceramics
Vitromex USA
Reports environmental footprint of generic CERAMIC TILE produced in North America
Participating manufacturers:

## Slide 63
INDUSTRY-WIDE EPD | MORTAR (2022)
Ardex
Bostik
Cemenquin/Cement Pro LLC
Crest
Custom Building Products
HB Fuller/TEC
Interceramic
Laticrete
Mapei
Parex
Schluter
Reports environmental footprint of generic CEMENT MORTAR FOR TILE INSTALLATION produced in North America
Participating manufacturers:

## Slide 64
INDUSTRY-WIDE EPD | GROUT (2022)
Ardex
Bexel
Bostik
Crest
Custom Building Products
HB Fuller/TEC
Interceramic
Laticrete
Mapei
Cemix/Texrite
Reports environmental footprint of generic CEMENT GROUT FOR TILE INSTALLATION produced in North America
Participating manufacturers:

## Slide 65
INDUSTRY-WIDE EPD | TILE
ANSI A137.1 mosaic, quarry, pressed floor, glazed wall, and porcelain tile
Industry-average EPD
Cradle-to-grave

## Slide 66
INDUSTRY-WIDE EPD | TILE
1.4
According to Part A of the PCR, the Estimated Service Life (ESL) of the building is assumed to be 75 years. Since ceramic tiles are expected to last as long as the building itself, the Reference Service Life (RSL) of ceramic tiles is taken to be 75 years.

## Slide 67
INDUSTRY-WIDE EPD | TILE
Transportation to building site
Installation into the building
Maintenance
End of life
GWP is measured in kg/m2
Raw material extraction
Manufacturing

## Slide 68
INDUSTRY-WIDE EPD | TILE
LCA Results

## Slide 69
LVT AND LVP ENVIRONMENTAL IMPACT | RELATIVE TO CERAMIC TILE
Vinyl tile: 2x higher than ceramic tile
Global warming potential
Rigid core: 3x higher than ceramic tile
Fossil fuel resource depletion
Vinyl tile: 3x higher than ceramic tile
Rigid core: 5x higher than ceramic tile
Additionally, higher potential for acidification, eutrophication, smog formation, and ozone depletion
Based on 75-year data reported in UL-certified industry-wide EPDs for Vinyl Tile and Rigid Core
Source: TCNA
Notes: Ocean acidification refers to a reduction in the pH of the ocean over an extended period time, caused primarily by uptake of carbon dioxide ...
Harmful algal blooms, dead zones, and fish kills are the results of a process called eutrophication — which occurs when the environment becomes enriched with nutrients, increasing the amount of plant and algae growth to estuaries and coastal waters.

## Slide 70
PCR NONCONFORMANCE | EXAMPLE OF CARPET TILE REPORTING OMISSION
Repair, replacement, refurbishing impacts are omitted.
Use/maintenance impact for product life (15-yr) and building life (75-yr) are not reported.
Use/maintenance impact only reported for 1 year.
Notes: Note: this is a product-specific declaration of a carpet tile manufacturer

## Slide 71
PCR NONCONFORMANCE | EXAMPLE OF LVT REPORTING OMISSION
Repair, replacement, refurbishing impacts are omitted.
Use/maintenance impact for product life (15-yr) and building life (75-yr) are not reported.
Use/maintenance impact only reported for 1 year.
Notes: Note: this is a product-specific declaration of a LVT manufacturer

## Slide 72
EPDs | TILE vs. OTHER FLOORING TYPES
Global Warming Potential (GWP) of North American-made ceramic tile EPD vs. EPDs for other flooring types
https://www.tcnatile.com/component/content/index.php?option=com_content&view=article&id=247
Notes: From Tile – The Natural Choice,
https://www.tcnatile.com/component/content/index.php?option=com_content&view=article&id=247

## Slide 73: PERFORMANCE OF
TILE & STONE ASSEMBLIES

## Slide 74
TCNA
INSTALLER QUALIFICATIONS | TCNA HANDBOOK LANGUAGE
Notes: This is taken from the 2012 TCNA Handbook

## Slide 75
“Journeyman Tile Layers Apprenticeship Programs… Contractors that employ union Journeymen Tile Setters can be found through the Union Locals that list their signatory contractors, primarily the Bricklayer and Allied Craftworkers (BAC)…
“Every aspect of a tile installation relies on the tile contracting company and its installers.”
“The following non-profit programs are well-established and recognized by the Handbook Committee:
“Tile Contractors’ Association of America (TCAA) Trowel of Excellence Program…”
“IMI Contractor College…
“Advanced Certification for Tile Installers (ACT)”
TCNA
INSTALLER QUALIFICATIONS | TCNA HANDBOOK LANGUAGE

## Slide 76
Dozens of factors contribute to the performance and durability of a stone installation. These factors can be categorized by the variability of materials, methods, and applications. To predict performance, we must understand:
WHAT is being installed?
HOW is it being installed?
WHERE is it being installed?
(How will it be used?)
WHO are the installers?
PERFORMANCE

## Slide 77
PERFORMANCE | HOW IS IT BEING INSTALLED?
PERFORMANCE | WHAT IS BEING INSTALLED?
PERFORMANCE | WHERE IS IT BEING INSTALLED?
PERFORMANCE | WHO ARE THE INSTALLERS?
Notes: From Tile – The Natural Choice,
https://www.tcnatile.com/component/content/index.php?option=com_content&view=article&id=247

## Slide 78
Limestone
Travertine
Onyx
Marble
Granite
Slate
Quartzite
Serpentine
Sandstone
Aesthetics
Strength
Density
Hardness
Absorption
Abrasion resistance
Bond strength
Thermal shock
Freeze/thaw cycling
Impact resistance
PROPERTIES
Basalt
PERFORMANCE | WHAT IS BEING INSTALLED?

## Slide 79
Subcommittee C18.03 on Material Specifications
ASTM C503
Standard Specification for
Marble Dimension Stone
ASTM C568
Standard Specification for
Limestone Dimension Stone
ASTM C615
Standard Specification for
Granite Dimension Stone
ASTM C616
Standard Specification for
Quartz-Based Dimension Stone
ASTM C629
Standard Specification for
Slate Dimension Stone
ASTM C1526
Standard Specification for
Serpentine Dimension Stone
ASTM C1527
Standard Specification for
Travertine Dimension Stone
ASTM Committee C18 on Dimension Stone
PERFORMANCE | WHAT IS BEING INSTALLED?
Notes: Subcommittees and Standards
Standards under the jurisdiction of C18
Each main committee in ASTM International is composed of subcommittees that address specific segments within the general subject area covered by the technical committee. Click on the subcommittee links below to see the title of existing standards for each subcommittee. Then, click on the resulting titles to see the standard's scope, referenced documents, and more.
C18.01 Test Methods
C18.03 Material Specifications
C18.06 Attachment Components and Systems
C18.07 Environmental Properties, Behavior, and Cleaning
C18.08 Selection of Dimension Stone
C18.90 Executive
C18.91 Nomenclature and Definitions

## Slide 80
ASTM C568 Standard Specification for Limestone
PERFORMANCE | WHAT IS BEING INSTALLED?
Notes: The modulus of rupture (MOR), also known as bending strength or flexural strength, measures the strength of a material before it breaks under bending stress. It's essentially a gauge of how much stress a material can withstand before it ruptures or fractures.
Here's a more detailed explanation:
What it measures:
MOR specifically quantifies the stress at the point of failure when a material is subjected to a bending load.
How it's used:
MOR is often used to determine the overall strength of materials like wood or concrete, and it can also be applied to other materials like tiles.
Why it matters:
High MOR values indicate that a material is more resistant to breakage under bending loads, making it suitable for applications where durability and strength are crucial, according to Infinita Lab.
Relationship to tensile strength:
In some cases, especially with concrete, the MOR can be significantly higher than the material's direct tensile strength, meaning the material is stronger under bending than under a direct pull.

## Slide 81
PERFORMANCE | HOW IS IT BEING INSTALLED?
PERFORMANCE | WHAT IS BEING INSTALLED?
PERFORMANCE | WHERE IS IT BEING INSTALLED?
PERFORMANCE | WHO ARE THE INSTALLERS?
Notes: From Tile – The Natural Choice,
https://www.tcnatile.com/component/content/index.php?option=com_content&view=article&id=247

## Slide 82
TCNA
As important as it is to have durable tiles, it is also imperative that the tile and everything behind it function together as a durable assembly.
Let’s look at how tile assemblies are described in the TCNA Handbook.
Method no.
F122 - STONE
PERFORMANCE | HOW IS IT BEING INSTALLED?
Notes: As important as it is to have durable tiles, it is also imperative that the tile and everything behind it function together as a durable assembly.

## Slide 83
TCNA
Method no.
F122 - STONE
Interior floor over on-ground concrete w/ waterproof membrane and natural stone tile
Method description
PERFORMANCE | HOW IS IT BEING INSTALLED?

## Slide 84
Method no.
Service rating
F122 - STONE
Interior floor over on-ground concrete w/ waterproof membrane and natural stone tile
Moderate
TCNA
Method description
PERFORMANCE | HOW IS IT BEING INSTALLED?

## Slide 85
TCNA
Each stone tile floor assembly in the TCNA Handbook is assigned a service rating (A.K.A. performance rating). These service ratings indicate how well the assembly will perform.
There are five service rating designations for stone tile floor assemblies in the TCNA Handbook, each correlating to a category of use based on the types of loads expected:
Service Ratings
PERFORMANCE | HOW IS IT BEING INSTALLED?

## Slide 86
Extra Heavy
Extra heavy and high-impact use in food plants, dairies, breweries, and kitchens. Requires quarry tile, packing house tile, or tile designated by the tile manufacturer for the intended application.
Residential
Residential kitchens, bathrooms, and foyers.
Heavy
Shopping malls, stores, commercial kitchens, work areas, laboratories, auto showrooms, and service areas, shipping/receiving areas, and exterior decks.
TCNA
Moderate
Normal commercial and light institutional use in public spaces of restaurants and hospitals.
Light
Light commercial use in office spaces, reception areas, kitchens, and bathrooms.
PERFORMANCE | SERVICE RATINGS

## Slide 87
3-wheel triangle-shaped cart loaded with weights
3/4 hp motor that drives the cart at 15 RPM
Loading schedule comprises 14 cycles; each cycle has specified type of wheels (soft rubber, hard rubber, steel), amount of weight to be stacked, and total revolutions to be executed.
Swivel caster wheels are equally spaced 15 in. from cart’s center
Floor is visually examined after each cycle for chipped tiles, broken tiles, loose tiles, popped grout joints, cracked grout joints, powdered grout joints
Standard Test Method for Evaluating Ceramic Floor tile Installation Systems Using the Robinson-Type Floor Tester
PERFORMANCE | ROBINSON FLOOR TEST
Notes: Test that provides indication of durability of the floor tile assembly
Informs the service category for the floor tile assembly

## Slide 88
Floor is visually examined after each cycle for chipped tiles, broken tiles, loose tiles, popped grout joints, creaked grout joints, powdered grout joints
Standard Test Method for Evaluating Ceramic Floor tile Installation Systems Using the Robinson-Type Floor Tester
PERFORMANCE | ROBINSON FLOOR TEST

## Slide 89
Residential
Kitchens, bathrooms, and foyers
Moderate
Normal commercial and light institutional use in public space of restaurants and hospitals
Light
Light commercial use in office space, reception areas, kitchens, bathrooms
Heavy
Shopping malls, stores, commercial kitchens, work areas, laboratories, auto showrooms, and service areas, shipping/receiving, exterior decks
Extra Heavy
Extra heavy and high-impact use in food plants, dairies, breweries, and kitchens. Requires quarry tile, packing house tile, or tile designated by tile manufacturer.
PERFORMANCE | ROBINSON FLOOR TEST

## Slide 90
PERFORMANCE | HOW IS IT BEING INSTALLED?
PERFORMANCE | WHAT IS BEING INSTALLED?
PERFORMANCE | WHERE IS IT BEING INSTALLED?
PERFORMANCE | WHO ARE THE INSTALLERS?
Notes: From Tile – The Natural Choice,
https://www.tcnatile.com/component/content/index.php?option=com_content&view=article&id=247

## Slide 91
TCNA
Method no.
F122 - STONE
Interior floor over on-ground concrete w/ waterproof membrane and natural stone tile
Method description
Environmental Exposure Classification
Res 1, 2, 3, 5 Com 1, 2, 3, 5
PERFORMANCE | WHERE IS IT BEING INSTALLED?

## Slide 92
Com1 (Commercial Dry)
Tile surfaces that will not be exposed to moisture or liquid except for cleaning purposes. Examples: floors in areas with no direct access to the outdoors and no wet utility function such as hallways, dry area ceilings, accent walls, and corridor walls.
TCNA
Com2 (Commercial Limited Water Exposure)
Tile surfaces that are subjected to moisture or liquids but do not become soaked or saturated. Examples: floors where water exposure is limited and/or water is removed, as in bathrooms and locker rooms. Some backsplashes, bathroom walls, other walls, and wainscots may also fall in this category.
Com3 (Commercial Wet)
Tile surfaces that are soaked, saturated, or regularly and frequently subjected to moisture or liquids. Examples: shower and tub floors and walls, enclosed pool areas, natatoriums, public communal showers, and some commercial kitchen floors and walls.
Com4 (Commercial High Humidity,
Heavy Moisture Exposure)
Tile surfaces that are subject to continuous high humidity or heavy moisture exposure, especially in enclosed areas. Examples: continuous use steam showers and steam room walls and ceilings.
Com5 (Commercial High Temperature ≥125°F)
Tile surfaces frequently subjected to water or vapor greater than or equal to 125°F. Examples: commercial saunas, furnace and boiler areas, and some commercial kitchen floors and walls.
Com6 (Commercial Exterior)
Tile surfaces exposed to exterior conditions. Examples: exterior walls, balconies, and decks.
Com7 (Commercial Submerged)
Tile surfaces exposed to continuous water submersion in interior or exterior conditions. Examples: swimming pools, water features, and fountains.
ENVIRONMENTAL EXPOSURE CLASSIFICATIONS

## Slide 93
PERFORMANCE | HOW IS IT BEING INSTALLED?
PERFORMANCE | WHAT IS BEING INSTALLED?
PERFORMANCE | WHERE IS IT BEING INSTALLED?
PERFORMANCE | WHO ARE THE INSTALLERS?
Notes: From Tile – The Natural Choice,
https://www.tcnatile.com/component/content/index.php?option=com_content&view=article&id=247

## Slide 94
The tile & stone industry has well-established benchmarks to help identify contractors and installers with the qualifications necessary to provide durable and long-lasting installations.
Requirements for minimum levels of competence can be written into a project’s specifications to ensure appropriate installation.
Installers who hold an Advanced Certifications for Tile Installers (ACT) certification have demonstrated outstanding technical efficiency.
The International Masonry Industry Training and Education Foundation (IMTEF) delivers comprehensive tile training for pre-apprentice, apprentice, and journeyworker tile setters and finishers.
Natural Stone Institute (NSI) Accreditation for Natural Stone Tile Installation. Contractors are evaluated with regard to best practices in installation and safety.
TCAA’s Trowel of Excellence certification distinguishes best practice tile contractors who are signatory with the International Union of Bricklayers and Allied Craftworkers (BAC).
PERFORMANCE | WHO ARE THE INSTALLERS?
Notes: Even if you have good material selection, appropriate installation methods, and consideration of environmental exposure, the assembly may still fail if not installed by qualified labor.
So far, we have examined the contributions to durability made by good material selection, appropriate installation methods, and consideration of environmental exposure. Even if all these boxes are checked, if qualified labor is not used to install it, the assembly may still fail over time. Fortunately, the tile industry has well-established benchmarks to help identify tile contractors and installers with the qualifications necessary to provide durable and long-lasting installations. TCAA’s Trowel of Excellence certification distinguishes best practice tile contractors who are signatory with the International Union of Bricklayers and Allied Craftworker (BAC). The International Masonry Industry Training and Education Foundation (IMTEF) delivers comprehensive tile training for pre-apprentice, apprentice, and journeyworker tile setters and finishers. Installers who hold an Advanced Certifications for Tile Installers (ACT) certification have demonstrated outstanding technical efficiency. Requirements for minimum levels of competence can be written into a project’s specifications to ensure appropriate installation.

## Slide 95
If the WHAT, HOW, WHERE, and WHO of installation are optimized, then natural stone will last 100 years or more.
A “cradle-to-grave” Life Cycle Analysis (LCA) should be considered in the Environmental Product Declaration (EPD)
PERFORMANCE | LCAs & EPDs

## Slide 96
INSTALLER QUALIFICATIONS | MASTERSPEC LANGUAGE

## Slide 97
Lavatory Renovation, Minneapolis, MN
INSTALLER QUALIFICATIONS | PROJECT SPECIFICATIONS
Installer employs at least one installer for Project that has completed the Advanced Certification for Tile Installers (ACT) certification for installation of membranes, shower receptors.
A. Installer Qualifications:
1.05 QUALITY ASSURANCE

## Slide 98
INSTALLER QUALIFICATIONS | ACT CERTIFICATIONS
B415
B421
B421C

## Slide 99
ACT-certified Installer
Pass hands-on skills assessment
3.
Pass written exam based on TCNA & ANSI Standards
2.
BAC journeyman/
apprentice or
certified by CTEF
1.
Experienced installer
BAC apprenticeship
or CTI certification
Orientation class
Study materials provided
Open-book test
Minimum passing grade 84%
Tests are widely available
Judged by certified evaluator
Judged on critical points
Testing and criteria are consistent
Certified in one or more skills
Certification good for 5 years
Credential is held by the installer
INSTALLER QUALIFICATIONS | ACT CERTIFICATIONS

## Slide 100
Maintain uniform grout joint width
Apply mortar to 80% coverage, min.
Determine areas of floor that are not flat
Maintain minimum lippage
Lay out tile on 33% offset
Correct substrate to acceptable flatness
CRITICAL POINTS | LARGE FORMAT TILE
Notes: - Flattening a substrate is trickier than it sounds. The demands are stringent.
- Tiles are set with a 33% offset per A108.02.4.3.8 for large format tile.
- Grout joint width 1/8” as rectified tile is being used. If a calibrated tile was used, the minimum grout joint size would be 3/16”
Lippage do to workmanship, must be limited to 1/32”
Mortar coverage is paramount for tile installations 80% minimum for dry areas, and 95% in wet areas

## Slide 101
Return membrane vertically at walls
Proper inside & outside corner connections
Fabric fully embedded @ liquid
Correct wet mil thickness @ liquid
Pre-treat corners, drain, & pipe
Seam min. 2” overlap @ sheet
Proper adhesive coverage @ sheet
CRITICAL POINTS | MEMBRANES
Notes: Application of both liquid applied A118.10, and sheet A118.12 membranes
A118.10 = Waterproof Membrane
A118.12 Crack Isolation Membrane also know as Anti-Fracture Membrane
Attachment to the drain bodies are critical points
Preparation of the substrate to receive the membranes is a must
There are specific ways to connect to a protrusion to ensure water integrity
Proper use of specific pieces of sheet membrane at inside and outside corners are required to be installed

## Slide 102
Cleavage membrane intact and properly overlapped
Wire reinforcement properly overlapped and suspended in mortar bed
Mortar bed flat, level, and thickness as specified
CRITICAL POINTS | MUD FLOORS
Notes: Cleavage membrane requires a 4” overlap, and to be lapped in the direction of the mortar installation.
Reinforcement wire is to be “suspended” within the mortar, and not to be touching the substrate or the top of the mortar bed.
Mortar is to be floated level, and up to 1-1/2” thick minimum of 1-1/4” -
Mortar must be flat to within 1/8” in 10’ and 1/16” in 24”.

## Slide 103
Metal lath installed shingle-fashion w/ proper laps, cut at inside corner
Cleavage membrane intact & installed shingle-fashion proper laps, folded at corners
Mortar applied to specified thickness
Inside & outside corners are square
All walls are plumb and floated to exact dimensions
CRITICAL POINTS | MUD WALLS
Notes: Cleavage membrane to be overlapped 2” “shingle fashion”, with no rips or tears
Wire reinforcement to be lapped 2”
Mortar must be between 3/8” and 3/4” thick
Mortar must be flat to within 1/4” in 10’, and plumb, level, and square
Entire project must be made to specific dimensions and sizes
Movement joints to be clear to the cleavage membrane. No wire, or mortar per EJ171

## Slide 104
Pre-slope installed w/ cont. flat slope
Sheet membrane wraps curb completely; curb is parallel to back wall and sloped to drain
Mortar bed has proper thickness and slope
Sealant between membrane & drain flange; Weep holes protected
No fasteners in membrane, vapor retarder, or backer board lower than 3” above finish curb
Sheet membrane installation passes flood test
CRITICAL POINTS | SHOWER RECEPTORS
Notes: Pre-sloped base has 1/4” per foot continuous slope.
Sheet membrane must be properly attached to drain. Weep holes must be kept clear of mortar.
Sheet membrane installed with correct fastener placement, overlap, and correct sealant application.
Vapor barrier to overlap on to the Sheet waterproofing. CBU to be correctly installed, i.e., screw pattern, and movement joints at interior corners
Curb installed square, even, and sloped towards pan
Pan must be floated with a flat continuous sloped plane at 1/4”/ft from the furthest point out to the drain

## Slide 105
Maintain minimum lippage
Grout joint cleaned to proper depth
Perimeter abutments free of grout for EJ
Determine out-of-flat areas in wall and floor, and correct accordingly
Trowel mortar on substrate & tile in one direction, parallel to short side of tile
Clean & accurate cuts around openings
Proper tile embedment techniques for wall and floor tile
CRITICAL POINTS | GAUGED PORCELAIN TILE & GPT PANELS
Notes: Substrate must be flat to within 1/8” in 10’ & 1/16 in 24”
Mortar combed in same direction across both tile and substrate
Tile panels are to have no lippage, and align with all other adjoining panels
Walls and floor are to be square to each other
All edges are to be smooth and have even transition between panels.

## Slide 106
A118.6 cement grout, sanded
A118.7 high performance cement grout
A118.6 cement grout, unsanded
A118.3 epoxy grout
Cement grout joints applied flush
Epoxy grout joints applied to proper depth
Expansion joints free of grout; backer rod & sealant properly installed
Finish free of smears & grout haze
CRITICAL POINTS | GROUTS
Notes: - Four different tile types, each with dissimilar characteristics, and different size joints.
A118.3 Epoxy grout in the Quarry.
A118.6 Standard sanded grout in the Brick Veneer, and un-sanded grout in the 4-1/4” glazed ceramic
A118.7 High Performance Grout in the 6x6 porcelain tile
All grouts must be correctly mixed, and applied according to manufactures recommendations
A118.6 Standard Cement Grout, A118.7 High Performance Grout, A118.3 Epoxy Grout Fusion / Plasma / True Color / FlexColor are all considered a single component Polymer Resin Grout- No product or installation standard for these types of grout.

## Slide 107
CONCLUSION
Thank you!
Please make sure you signed the attendance sheet (AIA members and non-AIA members)
Don’t forget to take a certificate if you need one for self-reporting
If you have a project or technical question re. masonry or tile you’d like to discuss, please contact us:
SCOTT CONWELL, FAIA SCONWELL@IMIWEB.ORG
Let’s connect on LinkedIn